## Slide 1: Embedded System Design
Project Overview
Igor Janjic
Leah Krynitsky
Brian Hilnbrand
Danny Duangphachanh

## Slide 2: Component Communication
Sensor PIC
(PIC18F45J10)
Sensors
(GP2Y0A60SZLF)
I2C
(slave)
Motor PIC
(PIC18F45J10)
I2C
(slave)
I2C
(master)
Rover Master PIC
(PIC18F46J50)
WiFly
AN0 - AN8
Timer
Sabertooth Motor Controller
Q.E.2 (Right)
Q.E.2
(Left)
ARM System1
UART
External or hard-wired connection
Internal connection
Wireless connection
Train bus connection
1 System layout shown on next slide
2 Quadrature Encoder
I2C2
(master)
Accelerometer
(LSM303D)
I2C
(slave)

## Slide 3: Component Communication Cont.
I2C
(master)
I2C
(slave)
ARM Board
process pos data
Push Buttons
LEDs
LCD
ARM PIC
(PIC18F46J50)
Rover System1
WiFly
UART
WiFly
External or hard-wired connection
Internal connection
Wireless connection
Train bus connection
1 System layout shown on next slide
2 Quadrature Encoder
switch between tabs

## Slide 4: Sensor Selections & Specs
SHARP GP2Y0A60SZLF Analog Distance Sensor
  Measuring distance: 10 cm - 150 cm
  Recommended operating voltage: 2.7 V - 5.5 V
  Operating speed: 60 Hz (16.5 ± 3.7 ms update rate)
  Output voltage differential: ~ 3.0 V (3.6 V at 10 cm - 0.6 V at 150 cm)
LSM303D 3-Axis Accelerometer
  Supply Voltage: 2.16 V - 3.6 V
  I2C interface

## Slide 5: Sensor Analog Output vs. Distance
*Graph found in datasheet available at: http://www.pololu.com/file/0J812/gp2y0a60szxf_e.pdf

## Slide 6: Sensor Locations on Rover
Two sensors on each side of the rover for:
  Object/obstacle detection
  Direction calibration
  General Orientation of Rover
Two additional sensors on front side (center) spaced vertically for ramp detection

## Slide 7: Sensor Communication
Sensors hard wired to analog inputs of Sensor PIC (PIC18F45J10)
Analog data converted using Sensor PIC A/D module
Requests for data received via I2C from Rover Master PIC (PIC18F46J50)
10-bit digital result sent to Rover Master PIC via I2C
Data relayed to ARM PIC (PIC18F46J50) via WiFly and sent to ARM Board via I2C

## Slide 8: ARM Communication Overview
ARM and 45J50 PIC (address 0x4F) communicate via I2C
Sensor queries sent to PIC 0x4F
Sensor data received from PIC 0x4F
Sensor data processed
Sensor data displayed
Rover and/or ramp locations determined
Motor commands generated
Motor commands sent to PIC 0x4F

## Slide 9: ARM Tasks
IR00
.
.
.
AC0
I2C Monitor
Conductor
IR0 Timer
AC0 Timer
DataConductor
LCD
LCD Timer
Locate
Commander

## Slide 10: ARM Communication Sensor Data Protocol
Sensor queries are sent to PIC 0x4F via I2C
Query rate is set as a compile time parameter
For each query if no data is available, PIC 0x4F will reply with 0x00
Received sensor data is preprocessed in various threads depending on which sensor the data corresponds to
IR Sensors:
  IR threads receive 2 bytes where the first byte is the first 8 bits of the sensor data and the last byte is the last 2 bits of the IR0 data
  IR0 sensor located on the front of the rover spaced vertically
    IR00 thread sends 0x0A to begin a query for data
    IR01 thread sends 0x0B to begin a query for data
  IR1 sensor located on the front of the rover spaced horizontally
    IR10 thread sends 0x1A to begin a query for data
    IR11 thread sends 0x1B to begin a query for data

## Slide 11: ARM Communication Sensor Data Protocol (Cont)
IR Sensors:
  IR threads receive 2 bytes where the first byte is the first 8 bits of the sensor data and the last byte is the last 2 bits of the IR0 data
  IR2 sensor located on the right of the rover spaced horizontally
    IR20 thread sends 0x2A to begin a query for data
    IR21 thread sends 0x2B to begin a query for data
  IR3 sensor located at the back of the rover spaced horizontally
    IR30 thread sends 0x3A to begin a query for data
    IR31 thread sends 0x3B to begin a query for data
  IR4 sensor located on the left of the rover spaced horizontally
    IR40 thread sends 0x4A to begin a query for data
    IR41 thread sends 0x4B to begin a query for data
AC0 thread sends 0x5A to begin a query for data from accelerometer sensor 0
  AC0 thread receives 6 bytes (2 for each axis) in 2s compliment form

## Slide 12: ARM Communication Motor Command Protocol
Motor commands sent to PIC 0x4F via I2C
Commander thread sends 1 byte representing the command that the motor controller will execute and 1 byte representing the speed the command will be executed at
Then a query byte is sent that details whether or not the rover has hit an obstacle: 0x41:
  No obstacle encountered: 0x00
  Obstacle encountered: 0x01
Commands are separated into two groups depending on the distance granularity needed: fine and coarse
Fine commands:
  Rotate left by 5 degrees: 0x11
  Rotate right by 5 degrees: 0x12
  Move forward 1 centimeters: 0x13
  Move backward 1 centimeters: 0x13
Coarse commands
  Rotate left by 45 degrees: 0x21
  Rotate right by 45 degrees: 0x22
  Move forward 5 centimeters: 0x23
  Move backward 5 centimeters: 0x24
Speed:
  Execute command at a slow rate: 0x31
  Execute command at a medium rate: 0x32
  Execute command at a fast rate: 0x33

## Slide 13: ARM Algorithms Motor Command
Relevant object locations and the closest ramp location is sent to the Command thread
Rover has four states:
  Roam:
    Rover moves until it discovers a ramp or encounters an obstacle
  RampDiscover
    Rover will periodically rotate 360 degrees to scan for ramps
  RampMove
    Rover moves toward the ramp
    A sequential list of commands that get the rover to the ramp are kept in memory
    List is updated with new data and newly discovered objects
  RampEscal
    Rover aligns with the ramp and goes over it

## Slide 14: ARM Algorithms Data Integration and Routing
After incoming sensor data is received, it is sent to the DataConductor thread which further processes the data, integrates it, and routes it to the Locate thread, LCD thread, and Commander thread
Routes data at a rate determined by compile time parameters
Sends processed data to the LCD thread which displays it on appropriate tabs on the display
Sends processed IR sensor data to Locate thread
Sends processed AC sensor data to Commander thread
Integration algorithms:
  Filtering outliers
  Converts IR sensor voltages to distances
  Converts AC sensor voltages to angles

## Slide 15: ARM Algorithms Rover Localization
After incoming IR sensor data is processed it is sent to the Locate thread which locates the rover on the internally supplied map, locates nearby ramps, and sends this data to the LCD
Only data about relevant objects are sent to Commander thread
Rover localization:
  If an object is encountered it is appended to a list of currently known about objects
    Distances to the object and counterclockwise angles of the object (with respect to the front of the rover) are kept in memory
    List of currently known about objects are updated every time a new data point arrives.
    Periodically, the list is scanned and collections of objects representing the same physical thing are integrated
  The rover’s location is determined by using this list

## Slide 16: ARM Algorithms Ramp Discovery
Ramp Discovery:
  Ramp discovery is performed using data from IR0 sensor
  Only nearest ramp data is sent to Commander thread
  If a ramp is discovered it is appended to a list of currently known about ramps
    Distances to the ramp and counterclockwise angles of the ramp (with respect to the front of the rover) are kept in memory
    List of currently known about ramps are updated every time a new data point arrives from the DataConductor thread

## Slide 17: ARM Algorithms Displaying Data
DataConductor thread sends processed data to appropriate tabs on the LCD
Tabs can be toggled with the pushbutton (or maybe by swiping the touch screen)
  TAB0 displays the IR0 sensors voltages
  TAB1 displays the IR1 sensors voltages
  TAB2 displays the IR2 sensors voltages
  TAB3 displays the IR3 sensors voltages
  TAB4 displays the IR4 sensors voltages
  TAB5 displays the AC0 sensor voltage
  TAB6 displays a list of the distances to and angles from various objects the rover has encountered
  TAB7 displays a live map of the rover.

## Slide 18: Rover Master PIC Overview
Rover Master PIC communicates with ARM via WiFly and Sensor PIC and Motor PIC via I2C
Receives sensor data request from ARM
Reads sensor data message buffer for sensor data
Transmits sensor data to ARM
Receives motor commands from ARM
Transmits motor commands to Motor PIC

## Slide 19: Motor PIC Overview
Motor PIC and Rover Master PIC communicate via I2C
Receives motor commands from ARM via Rover Master PIC
Transmits motor commands as packets to Motor Controller on a single serial line
Receives data from Quadrature Encoders to verify speed and turning angle

## Slide 20: Motor Controller Operation
Sabertooth 2x12 Motor Controller
Receives motor command packet from Motor PIC
Will operate in Mode 4: Packetized Serial
  One-directional transmission
  9600 baud rate
  Packet format consists of:
    Address byte
    Command byte
    Data byte
    7-bit checksum

## Slide 21: Serial Packet Details
Address bytes are assigned by the DIP switch
Will use four possible commands
  Drive forward motor 1
  Drive backwards motor 1
  Drive forward motor 2
  Drive backwards motor 2
Data byte will determine the speed the motor will drive
  0 will have the motor go into power save mode
  127 will have the motor go full power
If checksum is incorrect, the data packet will not be acted upon

## Slide 22: Simulation Overview
Why simulate?
Simulation is a key tool for engineers to test parts of products without having the entire product in-hand.
Reduces development cost/time to a fraction of that of real testing.
What does it do?
Mimics communication between component and the rest of the system.
Does not actually emulate the rest of the system does, but generates fake data that could have been produced by the system.
Presents data flow in a human-readable manner.

## Slide 23: Simulation Overview

## Slide 24: Device Communication Protocol Message Overview
Header: “H[Message type][Payload length]”
Handshake: “X[Message Type]”
Payload: “P[Payload]”
Tail: “T”
Handshake: “R[Size of payload received]”

## Slide 25: Device Communication Protocol Message Types
Message Type | ID
MSGT_TIMER0 | 10
MSGT_TIMER1 | 11
MSGT_MAIN1 | 20
MSGT_OVERRUN | 30
MSGT_UART_DATA | 31
MSGT_I2C_DBG | 41
MSGT_I2C_DATA | 40
Message Type | ID
MSGT_I2C_RQST 42 | 42
MSGT_I2C_MASTER_SEND_COMPLETE | 43
MSGT_I2C_MASTER_SEND_FAILED | 44
MSGT_I2C_MASTER_RECV_COMPLETE | 45
MSGT_I2C_MASTER_RECV_FAILED | 46
MSGT_SENSOR_DATA | 50

## Slide 26: Device Communication Protocol Message Flow

## Slide 27: Questions? #YOLOSWAG777BEARIT #3BARE4U #NOSCOPE #BEARSBEETSBATTLESTARGALACTICA #EXPLODINGBEAR
Rover
Team 7
Source: http://s3.amazonaws.com/wootdesigncontestentries/2141848/d77b5595-1fbc-4d5e-bcf3-baef36755aa2.jpg